## Slide 1: Jupyter notebooks and their widgets
Jean Bilheux
Neutron Imaging Computer Instrument Scientist
Materials Engineering Group
Neutron Scattering Division
Development
ASM - 2023

## Slide 2: Table of Contents
Neutron imaging technique
Jupyter notebooks
Hands on using simple jupyter notebooks
Make a Jupyter notebook interactive
More advanced notebooks with widgets
Standalone interface
https://github.com/neutrons/asm_2023/tree/main/jean
Notes: Here is how we gonna spent the next 45 minutes.
I will start by showing you what I have been doing before joining the imaging team.
Then in the first part I will describe my work as an imaging software developer
In the second part, I will talk about my work as Embedded imaging software developer and you will see how much the *embedded* word is important.
Finally I will give my vision of the CIS position

## Slide 3: Neutron Imaging Technique
https://pan-learning.org/wiki/index.php/Introduction_to_neutron_scattering
Fission (Continuous)
Spallation (Pulsed)

## Slide 4: MARS
IMAGING (CG-1D)
Neutron beam
Detector (CCD)
Flight tube (He filled)
Sample table
Rotation stage
Beam stop
Gap between lines = 100 μm
Gap between lines = 20 μm
(HFIR layout figures are courtesy of Georg Ehlers )
Attenuation counts
HFIR Cold Guide Hall

## Slide 5: VENUS
A wavelength dependent imaging beamline with a detector position at 25m with a maximum field-of-view of 20 x 20 cm2 and a spatial resolution of ~ 100 m
Optimized for unique imaging capabilities:
  Bragg-edge imaging – quantitative interpretation of total cross-section provides crystalline structure characterization (cold neutrons ~ meV, 10 s time resolution)
  Resonance imaging – isotopic-sensitive spatially-resolved spectroscopy technique (epithermal neutrons ~ eV, 100 ns time resolution)
Science areas: energy materials such as electrochemistry in battery cells, materials science including additively manufactured alloys and superalloys behavior under stress (heat, pressure), nuclear materials, archaeometry, etc.
VENUS Completion Date: Summer 2024
Schematic (top) and photograph (left) of VENUS

## Slide 6: Bragg edge imaging
Resonance imaging
Material Behavior: Monitoring residual strain relaxation and preferred grain orientation of additively manufactured Inconel 625 by in-situ neutron imaging
Microstrain
A.S. Tremsin et al, Additive Manufacturing 46 (2021) 102130.
Material Elemental/Isotopic Content: 3D maps of elemental/isotopic distribution in objects.
Zhang Y., Transactions of the American Nuclear Society, (2018).
VENUS

## Slide 7: Jupyter notebooks
Notes: Presentation of what they are, how to get them, and to run them

## Slide 8: Hand-on – cropping a stack of images
PLAN
Load the images
Visualize
Select region to crop
Visualize result
Export new images
jean/exercises/1.notebook_without_widgets_example1.ipynb

## Slide 9: Hand-on – cropping a stack of images
PLAN
Load the images
Visualize
Select region to crop
Visualize result
Export new images
jean/exercises/1.notebook_without_widgets_example2.ipynb

## Slide 10: Hand-on – cropping a stack of images
PLAN
Load the images
Visualize
Select region to crop
Visualize result
Export new images
jean/exercises/1.notebook_without_widgets_example2.ipynb
User Input Errors
Location of data (typos, not familiar with file path string …)
Extension of input files (not .tiff, but .tif)
Number of files to visualize
Output folder (forget to change to example2 -> overwriting example1 folder)

## Slide 11: Hand-on – cropping a stack of images
NEW PLAN using widgets
Load the images
Visualize
Select region to crop
Visualize result
Export new images

## Slide 12: More advanced used of widgets
Topaz config file
  Create a config file, later used by a script
Timepix3
  Fitting Bragg peaks
  HDF5 MCP /SNS/SNAP/IPTS-30008/nexus/run58682_histo.h5
  time_shift=11876 / offset=1863 / Ta
  Range =[1.445, 2.474], Edge=[1.919, 2.143]
Registration
  IPTS-1992/shared/processed_data/02/normalized
iBeatles
  /SNS/VENUS/shared/SNAP_calibration_Ni_Powder

## Slide 13: Infos
Neutron imaging web site (https://neutronimaging.ornl.gov/)
  All notebooks tutorials
  Many “how to…” guides
List of ipywidgets (https://ipywidgets.readthedocs.io/en/latest/examples/Widget%20List.html)
My blog with many python tricks I found out over the years (https://jeanbilheux.wordpress.com/)
Useful python librairies
  pyqtgraph
  matplotlib
  numpy
  pandas
  scikit-image
  piillow
  ipywe